## Slide 1
Architecture overview
An experimentation testbed for industrial communication over private 5G (srsRAN + Open5GS) — used to study large-payload transport, teleoperation latency, and peer-to-edge offload. Precise timing is one instrument, not the purpose.
UE — robot compute
LiDAR + 5G modem
ROS2 client publishes PointCloud2
stamps capture_ns, send_ns
5G network (lab)
srsRAN O-CU / O-DU on USRP radios
Open5GS core, UPF / N6
the impairment under test
MEC edge server
ROS2 ingest node
stamps recv_ns, process_done_ns
processes the cloud
Uu
UPF
RAN — two sources
JSON tap: O-DU scheduler KPIs
E2 xApp: KPM + run-scoped RC
Outputs
per-frame CSV + 2 s aggregated snapshots
mec-cast-telemetry — the shared spine
64-byte TimingEnvelope · DelayStats with exact percentiles · clocks and PTP monitor · lock-free recorder
Logging service — PostgreSQL
Every component posts snapshots here; RUN_ID is the trace_id that joins UE, edge and RAN for one experiment.
PTP disciplines every measuring host over the management LAN — never the 5G user plane, which carries no time sync. What makes a cross-host delay valid is that both ends trace to the SAME grandmaster, not which daemon gets them there.

## Slide 2
Deployment — local (development)
One docker network, no hardware. Network impairment is simulated so the pipeline can be exercised end to end on a laptop.
lidar-client
synthetic PointCloud2
seed · num_points · rate_hz
netem sidecar
shares the client netns
delay · jitter · loss
middleware centre
zenoh-router or dds-discovery
MIDDLEWARE picks one
edge
ingest + processing
writes CSV
logging + postgres
postgres:16 has no host port — reachable only inside the compose network
runs/ (bind mount)
per-frame CSV lands on the host and survives docker compose down
Bring it all up:
make up-local
MIDDLEWARE=dds make up-local
make logs make down
Or one container per terminal:
$COMPOSE up --no-deps <service>
Two compose files are always passed together so the containers share one network.
The netem sidecar impairs the client's egress — modelling the 5G uplink without touching host networking.
Same containers as the lab; only the composition differs.

## Slide 3
Deployment — lab testbed
Four roles on four hosts. The impairment is now the real 5G uplink, and clock discipline becomes a hard requirement.
ue
lidar-client
behind the 5G modem
EDGE_HOST, MIDDLEWARE
gnb
ran-collector
beside the srsRAN O-DU
UDP :55555 or WS :8001
edge
router or DDS server + edge
the MEC app server
behind the UPF
infra
logging + postgres + admin
optional: RIC + E2 xApp
deploy this first
PTP grandmaster — management / backhaul LAN
One grandmaster for every measuring host; the daemon varies. srsRAN and Open5GS implement no 5G-TSN, so the user plane carries no time sync.
Deploy one role to one host:
bash deploy/lab/deploy.sh infra ops@infra-host
Start order: infra → edge → gnb → ue
Everything posts to the logging service, and the UE dials the edge's router.
The UE dials out across the UPF — no multicast discovery is possible on a cellular user plane.
Each role mounts /dev/ptp0 so timestamps come from the disciplined hardware clock.
Every snapshot records ptp.reliable, so analysis can filter by clock health after the fact.

## Slide 4
Infra services — logging and admin
Two first-party services on the infra host. Logging is where aggregated results land; admin is where runs are started and stopped.
HTTP API (/api/v1)
POST /logs one entry or a batch
GET /logs filter by service, level, time, trace_id
GET /stats counts by level and service
GET /health/ready 503 when the database is down
Batch insert is one round trip regardless of size:
INSERT … SELECT FROM unnest(…)
Data model — log_entries
timestamp · level · service · host · logger · message
context JSONB, GIN indexed — all metrics live here
trace_id = RUN_ID, joins every component of one run
severity numeric mirror of level, so min_level ranks
Keyset pagination on (timestamp, id) — a walk through a
busy table never skips or duplicates rows.
Admin — run control plane (:8099)
Nodes subscribe over WebSocket on startup and retry every
30 s. Runs are created, started and stopped from a page;
state machine, keep-alive, and workflow diagnostics.
Operational posture — both
No authentication on either — bind them to the management
LAN only. Admin can start and stop experiments, so its
blast radius is wider than the log store's.
Per-frame samples do NOT go here — that firehose goes to CSV under runs/<RUN_ID>/. Logging holds 2-second aggregated snapshots; admin holds run manifests as files, no database, so the page still works when PostgreSQL is down.

## Slide 5
ROS2 on the UE — client and renderer
Two nodes on the robot. Vanilla ROS2 application code; only the middleware underneath is unusual.
1 — generate
deterministic cloud from a seed
capture_ns stamped
2 — publish
raw, or G-PCC coded
send_ns stamped last
3 — record
sender-side CSV
snapshots to logging
4 — render
mec_cast/result from the edge
process_done_ns stamped
Test vectors are a controlled variable
seed 42 reproducible contents
num_points 5000 payload size — the main sweep
rate_hz 10.0 publish rate
pattern lidar_scan ten shapes: cube, sphere,
torus, helix, wireframe, swarm…
1.4x to 23.5x voxel compression,
which sets the return payload too
The timing envelope rides in-band as a message field, because rclpy exposes no per-publish attachments on either middleware.
The renderer is optional and off by default, so the one-way path stays byte-for-byte comparable with campaigns recorded before it existed.
With codec=gpcc both legs travel G-PCC coded: encoding counts in the sender delay, decoding in processing (ADR-0014).
Both stamps that bound the round trip are taken on this host: capture_ns by the client, process_done_ns by the renderer, off one CLOCK_REALTIME. That makes the renderer's e2e_ns the only end-to-end latency figure in the platform that owes nothing to PTP discipline, and an independent check on the clock offset the one-way metrics depend on.

## Slide 6
Edge — mec_cast_edge
Runs on the MEC application server. The first line of the callback is a timestamp; everything else follows from it.
recv_ns
stamped on arrival
before any work
process
decode, if G-PCC coded
centroid + voxel count
process_done_ns
stamped after work
record
CSV + snapshot
then optionally reply
Derived per sample
network = recv_ns − send_ns
e2e = process_done_ns − capture_ns
processing = process_done_ns − recv_ns
sender = send_ns − capture_ns
Statistics: Welford mean and stddev, exact windowed percentiles.
The hot path never blocks: samples go into a bounded lock-free ring, and a writer thread drains it.
A full ring drops the sample and counts it — dropping is always preferable to perturbing the measurement.
A separate uploader thread posts snapshots, so a stalled logging service cannot stall CSV writing.
With publish_result on, the voxel cloud already computed goes back to the UE on mec_cast/result, or coded losslessly on mec_cast/result_gpcc — after record(), so the edge's own sample is never delayed for the renderer's benefit.
Percentiles are exact over a sliding window, computed by sorting a copy off the hot path — not a streaming estimator. P² was rejected because its error is unbounded on multimodal distributions, and 5G latency under HARQ retransmission is exactly that.

## Slide 7
Middleware — Zenoh or Fast DDS
Chosen at deployment, the same on every host. The application stays vanilla ROS2; only the RMW swaps.
UE nodes
dial OUT to the edge host
centre on the edge host
Zenoh router, or Fast DDS Discovery Server
unicast only — no multicast anywhere
edge node
subscribes; same topics, same QoS
Concern on a 5G link
Links
Discovery across the UPF
Data path
A NAT at the UPF
Staying on the 5G link
Zenoh — MIDDLEWARE=zenoh
tcp :7448 (default) · quic :7449
clients of the router
the router relays every sample
traversed: the UE dials out
a client dials one address
Fast DDS — MIDDLEWARE=dds
udp (default) · tcp
Discovery Server :11811, never SPDP
peer to peer RTPS, udp 7400+ or tcp :7410
udp needs a routable UE; tcp dials out
DDS_INTERFACES pins the interfaces
One knob per deployment (ADR-0013). The image's entrypoint configures the RMW; the nodes never name one. Each node reports what it runs, the admin shows it per zone and flags a mix, and run.json records it — so Zenoh versus DDS over 5G is a recorded factor of every run, not a rebuild.

## Slide 8
Profile B — WebRTC through a relay on the edge
Video for teleoperation, from a sender on one UE to a receiver on another, measured where the 5G legs meet (ADR-0015).
Sender — UE
Node app + C++ addon
synthetic or camera video
WHIP, over the 5G uplink
Relay on the MEC edge
str0m, unmodified: RTP mode, ICE-lite, one UDP port
forwards without decoding
Receiver — UE
same client, role recv
renders or headless
WHEP, over the 5G downlink
A patched libwebrtc, prebuilt
The fork stamps every packet with a 16-byte RTP header
extension, capture_ns and send_ns, and makes every frame a
timing frame. Its release workflow builds linux-x64 and
macos-arm64; make fetch-libwebrtc downloads the pinned one.
The relay stays out of the measurement
It writes the sender's extension back unchanged, so the
receiver measures as it would with no relay, and passes
keyframe requests back to the sender. Clients dial out to it;
it forwards a frame in tens of microseconds.
Limits: no arm64 Linux clients (Chromium ships no clang for that host), no camera on macOS yet, and the relay advertises one address, RELAY_PUBLIC_IP. Peer-to-peer calls through the signaling server stay, as the baseline a relayed call is compared with.

## Slide 9
Profile B — three measuring points per frame
Joined on the frame's RTP timestamp, so one video frame splits into its uplink, forwarding, downlink and playout.
Sender
capture_ns, send_ns
in the RTP extension
WebRTC stats: bitrate, estimate
Relay — site 3
network_ns: the uplink alone
processing_ns: its forwarding
jitter, loss and RTT of both legs
Receiver — site 4
e2e_ns: glass-to-glass
jitter buffer, decode, render
freezes, NACKs, PLIs
Per frame: the platform's CSV schema, at the relay and the receiver.
Per stream, every second: WebRTC's own statistics in webrtc.csv at all three, and in the logging service.
tools/media_join.py splits each frame into its legs and attaches the streams' state.
Under the admin, a run with profile media recruits the relay, a sender and a receiver; the RAN sources join too.
The run's params set the stream and the video's size and rate.
run.json records the stream, the video and the libwebrtc release.
Every cross-host figure needs PTP on both hosts. WebRTC's clock is not CLOCK_MONOTONIC on macOS, so the fork converts against WebRTC's own clock; a Mac rarely has PTP, the lab's Linux hosts and edge do.

## Slide 10
RAN — two sources and run-scoped control
The JSON tap for depth, an E2 xApp for the standard path and for control — one data model, so analysis never asks which produced a row.
JSON tap — ran-collector
srsRAN metrics: UDP (≤ 24.x) or WebSocket
per-UE MCS, HARQ, BSR, SNR, scheduler delays
ran/kpi.csv + raw reports
One RAN data model
canonical names and units
Rust + Python normalisers, one vector file
tools/ran_join.py: per-frame join
E2 xApp — O-SC near-RT RIC
E2SM-KPM: six DRB metrics, ≥ 1 s
capabilities over an E2Port adapter
ran-kpm/kpi.csv
Run-scoped RC control — E2SM-RC slice PRB quota
A ran_policy belongs to a run: every action recorded in control.csv, reverted on stop, failure, replacement, admin loss and after a crash.
Cross-checked
Both sources measure UE throughput; the admin flags a gap.
A 25 % cap read 0.252 in KPM, 0.250 in the JSON tap.
Not yet verified
Against a srsRAN E2 agent and on the lab gNB.
Units marked verify in ran/schema/metrics.md.
ADR-0010 keeps both sources; ADR-0011 sets the control rules. Tested end to end against gnb-sim, without a radio.

## Slide 11
Applications and future work
What an experimentation testbed for industrial communication over private 5G is for.
Industrial robotics
ROS2 fleets on private 5G instead of cabling or Wi-Fi.
Offloading perception to a MEC server lets robots carry
less compute — but only if the latency budget is known
rather than hoped for.
Teleoperation
Remote driving, cranes, mining, inspection. The operator
needs a defensible glass-to-glass figure and its tail —
a p99 that occasionally doubles is a safety property,
not a statistic.
Vehicle to vehicle / V2X
Cooperative perception: vehicles sharing point clouds
through an edge server. Sensor sharing is only useful
if the data arrives inside the reaction window, which
is exactly what this measures.
Other latency-critical uses
Closed-loop motion control and AGV coordination
Drone swarms and remote inspection
AR / VR assistance on the factory floor
Haptics and force feedback, where budgets are tightest
Near-term platform work
Campaign: G-PCC at 1 mm and 1 cm over 5G
Latency versus payload-size sweeps
Campaign: Zenoh versus Fast DDS over 5G
Real LiDAR replacing the synthetic source
Research directions
PRB reservation for the LiDAR UE, via run-scoped RC
Closed loop: PRBs adjusted from application p99
Network slicing per application class
Correlating MAC-layer events with application tails
The common thread: each of these needs a number someone is willing to defend. Reproducibility artifacts — run identifiers, per-frame CSV and recorded clock health — are what turn a demonstration into evidence.